## Slide 1
PEEK: A Proactive Producer Mobility Management Scheme for ICN
Vignesh Sivaraman
Department of Electrical and Computer Engineering

## Slide 2: Motivation
Increase in mobile traffic
  CISCO forecasts eightfold increase between 2015-2020[1]
Consumer mobility is supported in NDN
Mobile producers
  Smartphones
  Vehicles
Support for producer mobility
[1] CISCO, “White paper: Cisco VNI Forecast and Methodology, 2015-2020,” Tech. Rep., July 2016.
Notes: Supporting mobility has become a basic requirement for any internet architecture

## Slide 3: Objectives
Support for producer mobility
A distributed approach
Respecting the principles of NDN
Notes: First and foremost objective is to enable producer mobility.
There are a few solutions proposed in the literature like rendezvous server, indirection server and so on. In contrast to these proposal, this work address the producer mobility in a distributed manner.
And finally, we would like to take care that our approach respects the core principles of NDN like hierarchical naming schemes, content-location decoupling, interest aggregation and so on.
To this end, we propose a forwarding strategy to support producer mobility.
A forwarding strategy is characteristically distributed in nature and the proposed approach only requires a minimal addition to the interest header.

## Slide 4: Producer Mobility Problem
Consumer
R1
R2
R4
R3
AP1
AP2
AP3
AP4

## Slide 5: Proposed forwarding strategy
Exploits the following properties
  Spatial locality
  Interest and data traverse the same path
Introduce “Hopcount Threshold” field in Interest header
Interest Format
Content Name
Selectors
Nonce
Guiders
Hopcount
Hopcount Threshold

## Slide 6: Proposed forwarding strategy
Interest generation (at the consumer)
Interest forwarding (at the router)
Data forwarding (at the router)

## Slide 7: Interest generation
Initialize the threshold to a default value
On timeout, decrease the threshold value
On receiving the data, set threshold to the default value

## Slide 8: Interest forwarding
At the router (when no match in CS nor in PIT)
  Case 1: Hopcount less than threshold
    Forward interest to the best face using FIB
  Case 2: Hopcount greater than threshold
    Probe interest to all neighbors
  Case 3: Hopcount greater than TTL
    Drop interest

## Slide 9: Data forwarding
Forward the data using PIT
Update the FIB for the data with incoming face
R
AP1
AP2

## Slide 10: An Example (Threshold=2 and No timeout)
Consumer
R1
R2
R4
R3
AP1
AP2
AP3
AP4
FIB Updated

## Slide 11: An Example (Threshold=2 and timeout)
Consumer
R1
R2
R4
R3
AP1
AP2
AP3
AP4
Timeout
Threshold=1
FIB Update
Threshold=2

## Slide 12: Determining the threshold
Formulation of the optimization problem
  Decision variable: Hopcount threshold
  Objective: Minimize the cost incurred (in terms of packets generated)
  Constraint: Bound on consumer experienced delay
Cost of flooding: Number of neighbors at a distance of k or less

## Slide 13: Simulation Results
Setup
  A tree network
  Leaves are the APs for the producer
  Randomly moving producer
  Simulating a human walk to a vehicle movement
  Probabilistic flooding to compare the performance[2]
[2] Y.-T. Yu, R. B. Dilmaghani, S. Calo, M. Sanadidi, and M. Gerla, “Interest propagation in named data manets” in IEEE CNC’13, January 2013, pp. 1118–1122.

## Slide 14: Simulation Results
Notes: 4.54
5.47

## Slide 15: Simulation Results
Notes: 4.54
5.47

## Slide 16: Simulation Results
Notes: 4.54
5.47

## Slide 17: Simulation Results
Notes: 4.54
5.47

## Slide 18: Conclusion
Addressed producer mobility problem
Hopcount based forwarding
  Spatial locality
  Data traverses the same path as interest
Router forwards the interest based on the hopcount

## Slide 19: Mathematical expressions
Decision variable: (hopcount threshold)
Objective function:
  Minimize
Constraints

## Slide 20: Mathematical expressions
Probability that the shortest path between producer and first flooding router is i.
: Complimentary CDF of
: Expected number of first hop neighbors
: Expected number of second hop neighbors
Time to live

## Slide 21: Mathematical expressions
Power law graphs